Cosimulation with MyHDL & Icarus Verilog
&
Verilator
10/16/16

Goal to create a vcd using verilator.

Cosimulation with MyHDL & Icarus Verilog,

Steps to create a MyHDL & Icarus Verilog cosimulation
Create tb_txuart.v
create module tb_txuart1;
this creates the signals of the verilog file to be cosimulated
instaniate the module

create
$from_myhdl
signals coming from myhdl
$to_myhdl
signals going to myhdl
Create test_txuart.py which has a module def
test_bench(args):
Need to create the signals that are to be tested
Need to define stimlus
Need to create a clkgen that will be returned to simulation

_prep_cosim(args, **sigs):
compile
cmd = "iverilog -o txuart ../txuart.v ./tb_txuart.v"
The file txuart created from iverilog command is found in Appendix C
cosimulation setup ...
cmd = "vvp -m ./myhdl.vpi txuart"
The file myhdl.vpi is compiled in the myhdl source
myhdl/cosimulation/icarus with the make command.

gtkwave of cosimulation

Appendix A cosimulation tb_txuart.v

`timescale 1ns/10ps

module tb_txuart1;

reg i_clk;
reg i_reset;

reg [29:0] i_setup;
reg i_break;
reg i_wr;
reg [7:0] i_data;

output wire o_uart;
output wire o_busy;

initial begin
    $dumpfile("vcd/txuart1.vcd");
    $dumpvars(0, tb_txuart1);
end

initial begin
    $from_myhdl(
        i_clk,
        i_reset,
        i_setup,
        i_break,
        i_wr,
        i_data
    );
    $to_myhdl(
        o_uart,
        o_busy
    );
end

txuart dut_txuart(i_clk, i_reset, i_setup, i_break, i_wr, i_data, o_uart, o_busy);

endmodule

Appendix B test_txuart.py
"""10/09/16
The example is from the openarty
Now a test bench is being generated to test
using myhdl & iverilog
"""
from __future__ import division
from __future__ import print_function
from myhdl import *
import os
import argparse
from argparse import Namespace
def test_bench(args):
    """Need to create the signals that are to be test
    """

    i_clk = Signal(bool(0))
    i_reset = Signal(bool(0))
    i_break = Signal(bool(0))
    i_wr = Signal(bool(0))
    o_uart = Signal(bool(0))
    o_busy = Signal(bool(0))
    i_setup = Signal(intbv(0)[30:])
    i_data = Signal(intbv(0)[8:])

    """Need to define stimlus"""
    @instance
    def stimlus():
i_reset.next = 1
for i in range(10):
yield i_clk.posedge
for i in range(10):
yield i_clk.posedge
i_reset.next = 0
yield i_clk.posedge

i_setup.next = 0x6c8
yield i_clk.posedge

i_wr.next = 1
yield i_clk.posedge

i_wr.next = 0
yield i_clk.posedge

i_data.next = 0x55
yield i_clk.posedge

i_wr.next = 1
yield i_clk.posedge

i_wr.next = 0
yield i_clk.posedge
for i in range(300):
yield i_clk.posedge
raise StopSimulation
    """Need to create a clkgen that will be returned to simulation
    """

    @always(delay(4))
    def clkgen():
i_clk.next = not i_clk

    """Need an instance of the test code"""

    tb_dut = _prep_cosim(args,i_clk=i_clk,i_reset=i_reset,i_setup=i_setup, \
    i_break=i_break,i_wr=i_wr,i_data=i_data,o_uart=o_uart,o_busy=o_busy)

    print("back from prep cosim")
    print("start (co)simulation ...")
    Simulation((tb_dut, clkgen, stimlus)).run()

def _prep_cosim(args, **sigs):
    """ prepare the cosimulation environment
    """
    print (" *%s" % (sigs))
    print("compiling ...")
    cmd = "iverilog -o txuart ../txuart.v ./tb_txuart.v"
    print(" %s" % (cmd))
    os.system(cmd)
    # get the handle to the
    print("cosimulation setup ...")
    cmd = "vvp -m ./myhdl.vpi txuart"
    print(" %s" % (cmd))
    cosim = Cosimulation(cmd, **sigs)
    print(" %s" % (cosim))
    return cosim

if __name__ == '__main__':
print("Running test...")
test_bench(Namespace())

Appendix C. txuart created with
#! /usr/local/bin/vvp
:ivl_version "10.1 (stable)" "(v10_1)";
:ivl_delay_selection "TYPICAL";
:vpi_time_precision - 11;
:vpi_module "system";
:vpi_module "vhdl_sys";
:vpi_module "v2005_math";
:vpi_module "va_math";
S_0x1a4fc40 .scope module, "tb_txuart1" "tb_txuart1" 2 6;
 .timescale -9 -11;
v0x1a8a610_0 .var "i_break", 0 0;
v0x1a8a6d0_0 .var "i_clk", 0 0;
v0x1a8a7a0_0 .var "i_data", 7 0;
v0x1a8a8a0_0 .var "i_reset", 0 0;
v0x1a8a970_0 .var "i_setup", 29 0;
v0x1a8aa60_0 .var "i_wr", 0 0;
v0x1a8ab30_0 .net "o_busy", 0 0, L_0x1a8b590; 1 drivers
v0x1a8ac00_0 .net "o_uart", 0 0, v0x1a89f90_0; 1 drivers
S_0x1a4ead0 .scope module, "dut_txuart" "txuart" 2 44, 3 109 0, S_0x1a4fc40;
 .timescale 0 0;
    .port_info 0 /INPUT 1 "i_clk"
    .port_info 1 /INPUT 1 "i_reset"
    .port_info 2 /INPUT 30 "i_setup"
    .port_info 3 /INPUT 1 "i_break"
    .port_info 4 /INPUT 1 "i_wr"
    .port_info 5 /INPUT 8 "i_data"
    .port_info 6 /OUTPUT 1 "o_uart"
    .port_info 7 /OUTPUT 1 "o_busy"
L_0x1a8b590 .functor BUFZ 1, v0x1a8a110_0, C4<0>, C4<0>, C4<0>;
L_0x7f521397d018 .functor BUFT 1, C4<0000>, C4<0>, C4<0>, C4<0>;
v0x1a51410_0 .net/2u *"_s0", 3 0, L_0x7f521397d018; 1 drivers
v0x1a88f50_0 .net *"_s3", 23 0, L_0x1a8aca0; 1 drivers
v0x1a89030_0 .net *"_s7", 23 0, L_0x1a8aee0; 1 drivers
L_0x7f521397d060 .functor BUFT 1, C4<0000>, C4<0>, C4<0>, C4<0>;
v0x1a89120_0 .net/2u *"_s8", 3 0, L_0x7f521397d060; 1 drivers
v0x1a89200_0 .var "baud_counter", 27 0;
v0x1a89330_0 .net "break_condition", 27 0, L_0x1a8afd0; 1 drivers
v0x1a89410_0 .var "calc_parity", 0 0;
v0x1a894d0_0 .net "clocks_per_baud", 27 0, L_0x1a8ad70; 1 drivers
v0x1a895b0_0 .net "data_bits", 1 0, L_0x1a8b110; 1 drivers
v0x1a89720_0 .net "dblstop", 0 0, L_0x1a8b1b0; 1 drivers
v0x1a897e0_0 .net "fixd_parity", 0 0, L_0x1a8b3f0; 1 drivers
v0x1a898a0_0 .net "i_break", 0 0, v0x1a8a610_0; 1 drivers
v0x1a89960_0 .net "i_clk", 0 0, v0x1a8a6d0_0; 1 drivers
v0x1a89a20_0 .net "i_data", 7 0, v0x1a8a7a0_0; 1 drivers
v0x1a89b00_0 .net "i_reset", 0 0, v0x1a8a8a0_0; 1 drivers
v0x1a89bc0_0 .net "i_setup", 29 0, v0x1a8a970_0; 1 drivers
v0x1a89ca0_0 .net "i_wr", 0 0, v0x1a8aa60_0; 1 drivers
v0x1a89e50_0 .var "lcl_data", 7 0;
v0x1a89ef0_0 .net "o_busy", 0 0, L_0x1a8b590; alias, 1 drivers
v0x1a89f90_0 .var "o_uart", 0 0;
v0x1a8a050_0 .net "parity_even", 0 0, L_0x1a8b4c0; 1 drivers
v0x1a8a110_0 .var "r_busy", 0 0;
v0x1a8a1d0_0 .var "r_setup", 29 0;
v0x1a8a2b0_0 .var "state", 3 0;
v0x1a8a390_0 .net "use_parity", 0 0, L_0x1a8b350; 1 drivers
v0x1a8a450_0 .var "zero_baud_counter", 0 0;
E_0x1a61f30 .event posedge, v0x1a89960_0;
L_0x1a8aca0 .part v0x1a8a1d0_0, 0, 24;
L_0x1a8ad70 .concat [ 24 4 0 0], L_0x1a8aca0, L_0x7f521397d018;
L_0x1a8aee0 .part v0x1a8a1d0_0, 0, 24;
L_0x1a8afd0 .concat [ 4 24 0 0], L_0x7f521397d060, L_0x1a8aee0;
L_0x1a8b110 .part v0x1a8a1d0_0, 28, 2;
L_0x1a8b1b0 .part v0x1a8a1d0_0, 27, 1;
L_0x1a8b350 .part v0x1a8a1d0_0, 26, 1;
L_0x1a8b3f0 .part v0x1a8a1d0_0, 25, 1;
L_0x1a8b4c0 .part v0x1a8a1d0_0, 24, 1;
    .scope S_0x1a4ead0;
T_0 ;
    %pushi/vec4 1, 0, 1;
    %store/vec4 v0x1a89f90_0, 0, 1;
    %end;
    .thread T_0;
    .scope S_0x1a4ead0;
T_1 ;
    %pushi/vec4 1, 0, 1;
    %store/vec4 v0x1a8a110_0, 0, 1;
    %end;
    .thread T_1;
    .scope S_0x1a4ead0;
T_2 ;
    %pushi/vec4 15, 0, 4;
    %store/vec4 v0x1a8a2b0_0, 0, 4;
    %end;
    .thread T_2;
    .scope S_0x1a4ead0;
T_3 ;
    %pushi/vec4 0, 0, 8;
    %store/vec4 v0x1a89e50_0, 0, 8;
    %end;
    .thread T_3;
    .scope S_0x1a4ead0;
T_4 ;
    %pushi/vec4 0, 0, 1;
    %store/vec4 v0x1a89410_0, 0, 1;
    %end;
    .thread T_4;
    .scope S_0x1a4ead0;
T_5 ;
    %wait E_0x1a61f30;
    %load/vec4 v0x1a89b00_0;
    %flag_set/vec4 8;
    %jmp/0xz T_5.0, 8;
    %pushi/vec4 1, 0, 1;
    %assign/vec4 v0x1a89f90_0, 0;
    %pushi/vec4 1, 0, 1;
    %assign/vec4 v0x1a8a110_0, 0;
    %pushi/vec4 15, 0, 4;
    %assign/vec4 v0x1a8a2b0_0, 0;
    %pushi/vec4 0, 0, 8;
    %assign/vec4 v0x1a89e50_0, 0;
    %pushi/vec4 0, 0, 1;
    %assign/vec4 v0x1a89410_0, 0;
    %jmp T_5.1;
T_5.0 ;
    %load/vec4 v0x1a898a0_0;
    %flag_set/vec4 8;
    %jmp/0xz T_5.2, 8;
    %pushi/vec4 0, 0, 1;
    %assign/vec4 v0x1a89f90_0, 0;
    %pushi/vec4 14, 0, 4;
    %assign/vec4 v0x1a8a2b0_0, 0;
    %pushi/vec4 0, 0, 1;
    %assign/vec4 v0x1a89410_0, 0;
    %pushi/vec4 1, 0, 1;
    %assign/vec4 v0x1a8a110_0, 0;
    %jmp T_5.3;
T_5.2 ;
    %load/vec4 v0x1a8a450_0;
    %inv;
    %flag_set/vec4 8;
    %jmp/0xz T_5.4, 8;
    %pushi/vec4 1, 0, 1;
    %assign/vec4 v0x1a8a110_0, 0;
    %jmp T_5.5;
T_5.4 ;
    %load/vec4 v0x1a8a2b0_0;
    %cmpi/e 14, 0, 4;
    %jmp/0xz T_5.6, 4;
    %pushi/vec4 15, 0, 4;
    %assign/vec4 v0x1a8a2b0_0, 0;
    %pushi/vec4 1, 0, 1;
    %assign/vec4 v0x1a8a110_0, 0;
    %pushi/vec4 1, 0, 1;
    %assign/vec4 v0x1a89f90_0, 0;
    %pushi/vec4 0, 0, 1;
    %assign/vec4 v0x1a89410_0, 0;
    %jmp T_5.7;
T_5.6 ;
    %load/vec4 v0x1a8a2b0_0;
    %cmpi/e 15, 0, 4;
    %jmp/0xz T_5.8, 4;
    %load/vec4 v0x1a89bc0_0;
    %assign/vec4 v0x1a8a1d0_0, 0;
    %pushi/vec4 0, 0, 1;
    %assign/vec4 v0x1a89410_0, 0;
    %load/vec4 v0x1a89a20_0;
    %assign/vec4 v0x1a89e50_0, 0;
    %load/vec4 v0x1a89ca0_0;
    %load/vec4 v0x1a8a110_0;
    %inv;
    %and;
    %flag_set/vec4 8;
    %jmp/0xz T_5.10, 8;
    %pushi/vec4 0, 0, 1;
    %assign/vec4 v0x1a89f90_0, 0;
    %pushi/vec4 1, 0, 1;
    %assign/vec4 v0x1a8a110_0, 0;
    %load/vec4 v0x1a895b0_0;
    %dup/vec4;
    %pushi/vec4 0, 0, 2;
    %cmp/u;
    %jmp/1 T_5.12, 6;
    %dup/vec4;
    %pushi/vec4 1, 0, 2;
    %cmp/u;
    %jmp/1 T_5.13, 6;
    %dup/vec4;
    %pushi/vec4 2, 0, 2;
    %cmp/u;
    %jmp/1 T_5.14, 6;
    %dup/vec4;
    %pushi/vec4 3, 0, 2;
    %cmp/u;
    %jmp/1 T_5.15, 6;
    %jmp T_5.16;
T_5.12 ;
    %pushi/vec4 0, 0, 4;
    %assign/vec4 v0x1a8a2b0_0, 0;
    %jmp T_5.16;
T_5.13 ;
    %pushi/vec4 1, 0, 4;
    %assign/vec4 v0x1a8a2b0_0, 0;
    %jmp T_5.16;
T_5.14 ;
    %pushi/vec4 2, 0, 4;
    %assign/vec4 v0x1a8a2b0_0, 0;
    %jmp T_5.16;
T_5.15 ;
    %pushi/vec4 3, 0, 4;
    %assign/vec4 v0x1a8a2b0_0, 0;
    %jmp T_5.16;
T_5.16 ;
    %pop/vec4 1;
    %jmp T_5.11;
T_5.10 ;
    %pushi/vec4 1, 0, 1;
    %assign/vec4 v0x1a89f90_0, 0;
    %pushi/vec4 0, 0, 1;
    %assign/vec4 v0x1a8a110_0, 0;
T_5.11 ;
    %jmp T_5.9;
T_5.8 ;
    %pushi/vec4 1, 0, 1;
    %assign/vec4 v0x1a8a110_0, 0;
    %load/vec4 v0x1a8a2b0_0;
    %parti/s 1, 3, 3;
    %pad/u 32;
    %cmpi/e 0, 0, 32;
    %jmp/0xz T_5.17, 4;
    %load/vec4 v0x1a89e50_0;
    %parti/s 1, 0, 2;
    %assign/vec4 v0x1a89f90_0, 0;
    %load/vec4 v0x1a89410_0;
    %load/vec4 v0x1a89e50_0;
    %parti/s 1, 0, 2;
    %xor;
    %assign/vec4 v0x1a89410_0, 0;
    %load/vec4 v0x1a8a2b0_0;
    %cmpi/e 7, 0, 4;
    %jmp/0xz T_5.19, 4;
    %load/vec4 v0x1a8a390_0;
    %flag_set/vec4 8;
    %jmp/0 T_5.21, 8;
    %pushi/vec4 8, 0, 4;
    %jmp/1 T_5.22, 8;
T_5.21 ; End of true expr.
    %pushi/vec4 9, 0, 4;
    %jmp/0 T_5.22, 8;
 ; End of false expr.
    %blend;
T_5.22;
    %assign/vec4 v0x1a8a2b0_0, 0;
    %jmp T_5.20;
T_5.19 ;
    %load/vec4 v0x1a8a2b0_0;
    %addi 1, 0, 4;
    %assign/vec4 v0x1a8a2b0_0, 0;
T_5.20 ;
    %pushi/vec4 0, 0, 1;
    %load/vec4 v0x1a89e50_0;
    %parti/s 7, 1, 2;
    %concat/vec4; draw_concat_vec4
    %assign/vec4 v0x1a89e50_0, 0;
    %jmp T_5.18;
T_5.17 ;
    %load/vec4 v0x1a8a2b0_0;
    %cmpi/e 8, 0, 4;
    %jmp/0xz T_5.23, 4;
    %pushi/vec4 9, 0, 4;
    %assign/vec4 v0x1a8a2b0_0, 0;
    %load/vec4 v0x1a897e0_0;
    %flag_set/vec4 8;
    %jmp/0xz T_5.25, 8;
    %load/vec4 v0x1a8a050_0;
    %assign/vec4 v0x1a89f90_0, 0;
    %jmp T_5.26;
T_5.25 ;
    %load/vec4 v0x1a89410_0;
    %load/vec4 v0x1a8a050_0;
    %flag_set/vec4 8;
    %jmp/0 T_5.27, 8;
    %pushi/vec4 1, 0, 1;
    %jmp/1 T_5.28, 8;
T_5.27 ; End of true expr.
    %pushi/vec4 0, 0, 1;
    %jmp/0 T_5.28, 8;
 ; End of false expr.
    %blend;
T_5.28;
    %xor;
    %assign/vec4 v0x1a89f90_0, 0;
T_5.26 ;
    %jmp T_5.24;
T_5.23 ;
    %load/vec4 v0x1a8a2b0_0;
    %cmpi/e 9, 0, 4;
    %jmp/0xz T_5.29, 4;
    %pushi/vec4 1, 0, 1;
    %assign/vec4 v0x1a89f90_0, 0;
    %load/vec4 v0x1a89720_0;
    %flag_set/vec4 8;
    %jmp/0xz T_5.31, 8;
    %pushi/vec4 10, 0, 4;
    %assign/vec4 v0x1a8a2b0_0, 0;
    %jmp T_5.32;
T_5.31 ;
    %pushi/vec4 15, 0, 4;
    %assign/vec4 v0x1a8a2b0_0, 0;
T_5.32 ;
    %pushi/vec4 0, 0, 1;
    %assign/vec4 v0x1a89410_0, 0;
    %jmp T_5.30;
T_5.29 ;
    %pushi/vec4 15, 0, 4;
    %assign/vec4 v0x1a8a2b0_0, 0;
    %pushi/vec4 1, 0, 1;
    %assign/vec4 v0x1a89f90_0, 0;
T_5.30 ;
T_5.24 ;
T_5.18 ;
T_5.9 ;
T_5.7 ;
T_5.5 ;
T_5.3 ;
T_5.1 ;
    %jmp T_5;
    .thread T_5;
    .scope S_0x1a4ead0;
T_6 ;
    %pushi/vec4 1, 0, 1;
    %store/vec4 v0x1a8a450_0, 0, 1;
    %end;
    .thread T_6;
    .scope S_0x1a4ead0;
T_7 ;
    %pushi/vec4 200000, 0, 28;
    %store/vec4 v0x1a89200_0, 0, 28;
    %end;
    .thread T_7;
    .scope S_0x1a4ead0;
T_8 ;
    %wait E_0x1a61f30;
    %load/vec4 v0x1a89200_0;
    %pushi/vec4 1, 0, 28;
    %cmp/e;
    %flag_get/vec4 4;
    %assign/vec4 v0x1a8a450_0, 0;
    %load/vec4 v0x1a89b00_0;
    %flag_set/vec4 8;
    %load/vec4 v0x1a898a0_0;
    %flag_set/vec4 9;
    %flag_or 9, 8;
    %jmp/0xz T_8.0, 9;
    %load/vec4 v0x1a89330_0;
    %assign/vec4 v0x1a89200_0, 0;
    %jmp T_8.1;
T_8.0 ;
    %load/vec4 v0x1a8a450_0;
    %inv;
    %flag_set/vec4 8;
    %jmp/0xz T_8.2, 8;
    %load/vec4 v0x1a89200_0;
    %subi 1, 0, 28;
    %assign/vec4 v0x1a89200_0, 0;
    %jmp T_8.3;
T_8.2 ;
    %load/vec4 v0x1a8a2b0_0;
    %cmpi/e 14, 0, 4;
    %jmp/0xz T_8.4, 4;
    %load/vec4 v0x1a894d0_0;
    %ix/load 4, 2, 0;
    %flag_set/imm 4, 0;
    %shiftl 4;
    %assign/vec4 v0x1a89200_0, 0;
    %jmp T_8.5;
T_8.4 ;
    %load/vec4 v0x1a8a2b0_0;
    %cmpi/e 15, 0, 4;
    %jmp/0xz T_8.6, 4;
    %load/vec4 v0x1a89ca0_0;
    %load/vec4 v0x1a8a110_0;
    %inv;
    %and;
    %flag_set/vec4 8;
    %jmp/0xz T_8.8, 8;
    %load/vec4 v0x1a894d0_0;
    %subi 1, 0, 28;
    %assign/vec4 v0x1a89200_0, 0;
    %jmp T_8.9;
T_8.8 ;
    %pushi/vec4 1, 0, 1;
    %assign/vec4 v0x1a8a450_0, 0;
T_8.9 ;
    %jmp T_8.7;
T_8.6 ;
    %load/vec4 v0x1a894d0_0;
    %subi 1, 0, 28;
    %assign/vec4 v0x1a89200_0, 0;
T_8.7 ;
T_8.5 ;
T_8.3 ;
T_8.1 ;
    %jmp T_8;
    .thread T_8;
    .scope S_0x1a4fc40;
T_9 ;
    %vpi_call 2 22 "$dumpfile", "vcd/txuart1.vcd" {0 0 0};
    %vpi_call 2 23 "$dumpvars", 32'sb00000000000000000000000000000000, S_0x1a4fc40 {0 0 0};
    %end;
    .thread T_9;
    .scope S_0x1a4fc40;
T_10 ;
    %vpi_call 2 27 "$from_myhdl", v0x1a8a6d0_0, v0x1a8a8a0_0, v0x1a8a970_0, v0x1a8a610_0, v0x1a8aa60_0, v0x1a8a7a0_0 {0 0 0};
    %vpi_call 2 35 "$to_myhdl", v0x1a8ac00_0, v0x1a8ab30_0 {0 0 0};
    %end;
    .thread T_10;
# The file index is used to find the file name in the following table.
:file_names 4;
    "N/A";
    "<interactive>";
    "./tb_txuart.v";
    "../txuart.v";