Cosimulation with MyHDL & Icarus Verilog
&
Verilator
10/16/16

Goal to create a vcd using verilator.

Cosimulation with MyHDL & Icarus Verilog,

Steps to create a MyHDL & Icarus Verilog cosimulation
Create tb_txuart.v
create module tb_txuart1;
this creates the signals of the verilog file to cosimulated
instaniate the module

create
$from_myhdl
signals coming from myhdl
$to_myhdl
signals going to myhdl
Create test_txuart.py which has a module def
test_bench(args):
Need to create the signals that are to be tested
Need to define stimlus
Need to create a clkgen that will be returned to simulation

_prep_cosim(args, **sigs):
compile
cmd = "iverilog -o txuart ../txuart.v ./tb_txuart.v"
cosimulation setup ...
cmd = "vvp -m ./myhdl.vpi txuart"

gtkwave of cosimulation

Appendix A cosimulation tb_txuart.v

`timescale 1ns/10ps

module tb_txuart1;

reg i_clk;
reg i_reset;

reg [29:0] i_setup;
reg i_break;
reg i_wr;
reg [7:0] i_data;

output wire o_uart;
output wire o_busy;

initial begin
    $dumpfile("vcd/txuart1.vcd");
    $dumpvars(0, tb_txuart1);
end

initial begin
    $from_myhdl(
        i_clk,
        i_reset,
        i_setup,
        i_break,
        i_wr,
        i_data
    );
    $to_myhdl(
        o_uart,
        o_busy
    );
end

txuart dut_txuart(i_clk, i_reset, i_setup, i_break, i_wr, i_data, o_uart, o_busy);

endmodule

Appendix B test_txuart.py
"""10/09/16
The example is from the openarty
Now a test bench is being generated to test
using myhdl & iverilog
"""
from __future__ import division
from __future__ import print_function
from myhdl import *
import os
import argparse
from argparse import Namespace
def test_bench(args):
    """Need to create the signals that are to be test
    """

    i_clk = Signal(bool(0))
    i_reset = Signal(bool(0))
    i_break = Signal(bool(0))
    i_wr = Signal(bool(0))
    o_uart = Signal(bool(0))
    o_busy = Signal(bool(0))
    i_setup = Signal(intbv(0)[30:])
    i_data = Signal(intbv(0)[8:])

    """Need to define stimlus"""
    @instance
    def stimlus():
i_reset.next = 1
for i in range(10):
yield i_clk.posedge
for i in range(10):
yield i_clk.posedge
i_reset.next = 0
yield i_clk.posedge

i_setup.next = 0x6c8
yield i_clk.posedge

i_wr.next = 1
yield i_clk.posedge

i_wr.next = 0
yield i_clk.posedge

i_data.next = 0x55
yield i_clk.posedge

i_wr.next = 1
yield i_clk.posedge

i_wr.next = 0
yield i_clk.posedge
for i in range(300):
yield i_clk.posedge
raise StopSimulation
    """Need to create a clkgen that will be returned to simulation
    """

    @always(delay(4))
    def clkgen():
i_clk.next = not i_clk

    """Need an instance of the test code"""

    tb_dut = _prep_cosim(args,i_clk=i_clk,i_reset=i_reset,i_setup=i_setup, \
    i_break=i_break,i_wr=i_wr,i_data=i_data,o_uart=o_uart,o_busy=o_busy)

    print("back from prep cosim")
    print("start (co)simulation ...")
    Simulation((tb_dut, clkgen, stimlus)).run()

def _prep_cosim(args, **sigs):
    """ prepare the cosimulation environment
    """
    print (" *%s" % (sigs))
    print("compiling ...")
    cmd = "iverilog -o txuart ../txuart.v ./tb_txuart.v"
    print(" %s" % (cmd))
    os.system(cmd)
    # get the handle to the
    print("cosimulation setup ...")
    cmd = "vvp -m ./myhdl.vpi txuart"
    print(" %s" % (cmd))
    cosim = Cosimulation(cmd, **sigs)
    print(" %s" % (cosim))
    return cosim

if __name__ == '__main__':
print("Running test...")
test_bench(Namespace())